## Slide 1: CLOS topology Static Routing Fabric

## Slide 2: Scenario
Small or Medium size topology under 64 switches.
Ares uses static route to maintain fabric and VxLAN between hosts to have L2 connectivity.
For
  Host basically using L3 to connect each other but skip the routing protocol.
  Hosts also want to have L2 connectivity.
  Have tenant concept in hosts.
Notes: Host NIC card can have two IPs, one for VxLAN tunnel target host, another for L3 routing.
Or Host NIC card using VLAN interface to assign IP.

## Slide 3: Server Requirement
A Server Which can run VM
  HW spec:
    At least 8G ram.
    At least 8 core a CPU.
    HD at leaf 20Gb
Get the VM
  http://124.219.108.10/Ares/mars_staticfabric.ova
  Useraccount/password: mars/mars

## Slide 4: Start Mars
1. Update this controller IP by using script “update_controller_ip.sh”
2. Start controller by script “restart_mars.sh”
3. After waiting some minutes according to VM CPU.
4. Login from Web browser: https://<controller_IP>
5. If mars can’t login, please check the docker logs. It shall has “End wait MARS boot”.
  docker logs mars
6. Mars is running by docker. Each new mars docker image has one day unlimited license.

## Slide 5: Login into your Mars
NOTE: You can visit our demo site https://210.63.204.29/ karaf/karaf
Login your Mars “ https://<your server IP> , default account/password is karaf/karaf

## Slide 6: Demo - Topology
Spine 1
Leaf 1
Leaf 2
VxLAN: 192.168.10.193/24
Host IP: 192.168.100.101/26
VxLAN: 192.168.10.195
Host IP: 192.168.200.201/26
32
32
HW:
Spine: AS7712
Leaf: AS5835
Spine 2
Case 1: Underlay auto provision
Case 2: VxLAN tunnel by EVPN
SW:
Edgecore-SONiC_20210505_054937_ec202006_205.bin

## Slide 7
Add device

## Slide 8
Input Necessary Information:
Device Name
Using which protocol to management
Device MAC (mgmt. port)
Management Address: Device IP and management port.
OS: chose sonic
MFR: chose ecsonic
Type: Spine or leaf

## Slide 9
After Added a device you can find our it try to connect in Available column.
Please keep add other devices as you want

## Slide 10
You can check the TOPO page to check the device link status

## Slide 11
Using special icon to display more information

## Slide 12
Provision Host segment for each host.

## Slide 13
Provision the necessary host segment information
Please use comma (,) to finish input port.

## Slide 14
Check the result, and using Ping to verify the connectivity between two hosts.

## Slide 15
Link page display each link was allocated which subnet

## Slide 16
Provision VxLAN tunnel for two VxLAN hosts.
Create tenant on switches
Add host to tenant on which switch

## Slide 17
Create tenant on switches

## Slide 18
Add hosts to tenant - 1

## Slide 19
Add hosts to tenant - 2

## Slide 20
Testing VxLAN hosts connectivity by ping another host